## Slide 1: Batch Scheduler Monitoring MVP
Objective Implement a lightweight monitoring solution for the lambda-crr-tm-scheduled AWS Lambda to provide real-time visibility of: • Technical failures • Functional/process failures • Batch scheduling issues Monitoring Flow AWS Lambda (lambda-crr-tm-scheduled) │ ▼ Amazon SNS │ ┌───────┴────────┐ │ │ Email Notification Microsoft Teams Channel

## Slide 2: Technical Failure Monitoring
Trigger Conditions Alerts are generated when unexpected runtime or infrastructure errors occur during Lambda execution. Examples • Database connectivity failures • Missing S3 objects (NoSuchKey) • API failures or timeouts • AWS permission issues • Python runtime exceptions (KeyError, parsing issues, etc.) Behavior • Lambda execution fails • Full traceback is captured • SNS alert is triggered • Email and Teams notifications are sent

## Slide 3: Functional Failure Monitoring
Trigger Conditions Alerts are generated when the scheduler detects business/process-level failures. Example completed failure Behavior • Lambda execution continues • Warning notification is generated • Contextual information is included: - filename - runId - batch status

## Slide 4: Implemented Solution
Lambda Enhancements (handler.py) • Added reusable SNS alerting function: send_failure_alert() • Added global exception monitoring • Added functional status monitoring • Added full traceback capture Amazon SNS Integration • Dedicated SNS topic: <project>-<env>-lambda-alerts • Configured subscriptions: - Operational email distribution - Microsoft Teams channel email IAM & Configuration • Added sns:Publish permission • Added SNS_TOPIC_ARN environment variable

## Slide 5: Current Outcome
Monitoring Capabilities Achieved • Real-time operational alerting • Technical failure visibility • Functional failure visibility • Teams integration • Centralized notification delivery • Improved operational response capability